Sketching with Hardware
06: Programming

---
Programming the Arduino
- Microcontrollers are restricted in memory and computing power
- Programs are written in C or C++
- Rather simple applications → simple programs
- Different patterns and paradigms than e.g. in Java

---
Basic Program Structure
// declare variables here
// the setup routine runs once on startup
void setup() {
}
// the loop routine runs over and over again forever:
void loop() {
}

---
Arduino-specific Functions
Function	Description
delay(int micros)	Delays the program by micros microseconds
pinMode(int pin, / int direction)	Defines a pin as INPUT or OUTPUT. Should be called during setup().
digitalRead(int pin)	Reads value from a pin. Returns HIGH (1) or LOW (0).
analogRead(int pin)	Reads analog value from a pin. Returns 0 to 255.
digitalWrite(int pin, / int value)	Sets a pin to either HIGH (5 V) or LOW (0 V).
analogWrite(int pin, / int value)	Sets voltage on a pin to a value between 0 (0 V) and 255 (5 V). Only works with pins that support PWM.
Serial.println(“Hello”)	Writes to the serial monitor and can be used for debugging. Call Serial.begin(9600) during setup().

---
Non-blocking code
- The Arduino can only run one thread at a time
- No parallelization of tasks
- The delay()-function blocks the whole program
- delay() can be avoided by using a timer

---
Simple Timer
int buttonPin = 5;
int ledPin = 13;
int ledState = LOW;
void loop() {
  // blink the LED
  if(ledState == LOW) {
    ledState = HIGH;
  }
  else {
    ledState = LOW;
  }
  // turn off LED if button is not pressed
  if(digitalRead(buttonPin) == LOW) {
    ledState = LOW;
  }
  digitalWrite(ledPin, ledState);
  delay(1000); // wait for a second
}
// ...
long lastMillis = 0;
void loop() {
  // check time since last update
  if(millis() - lastMillis >= 1000) {
    lastMillis = millis();
    if(ledState == LOW) {
      ledState = HIGH;
    }
    else {
      ledState = LOW;
    }
  }
  // turn off LED if button is not pressed
  if(digitalRead(buttonPin) == LOW) {
    ledState = LOW;
  }
  digitalWrite(ledPin, ledState);
}
blocking
non-blocking

---
Code Structure
- Arduino code is often simple and sequential
- Tends to get messy pretty fast
- Debugging code and hardware at the same time can be tedious
- Well-structured code leads to better readability and easier debugging

---
State Machine: Cookie Dispenser
#define WAIT 1
#define ORDER 2
#define PAYMENT 3
#define DISPENSE 4
int state = WAIT;
int order;
// cookie dispenser functions
int getInput() { … }
int getOrder() { … }
void handlePayment(int product) { … }
void dispenseProduct(int product) { … }
void loop() {
  switch(state) {
    case WAIT:
      if(getInput() != 0) state = ORDER;
      else delay(1000);
      break;
    case ORDER:
      order = getOrder();
      state = PAYMENT;
      break;
    case PAYMENT:
      handlePayment(order);
      state = DISPENSE;
      break;
    case DISPENSE:
      dispenseProduct(order);
      state = WAIT;
      break;
}

---
Debug Levels
- The Arduino IDE has no builtin debugger
- Serial output is used to log the state of programs
- Using debug levels lets you switch between different levels of verbosity quickly
#define NONE 0
#define ERROR 1
#define WARN 2
#define DEBUG 3
#define ALL 4
#define DEBUG_LEVEL WARN
void loop() {
  if(DEBUG_LEVEL >= WARN) {
    Serial.println(“Warning!”);
  }
}