Sketching with Hardware
08: Electronics 03 (Digital Electronics)

---
Analog vs Digital
Analog
Digital

---
Pros and Cons of Digital Signals
- Clearly defined – either there is voltage or not
- Less prone to errors and noise
- Can be saved and reproduced easily
But:
- Less information than analog “original”
- Digital components are more complex

---
Pulse Width Modulation (PWM)
Digital “simulation” of analog signal
U = U_{ HIGH } * {{ t_{1} } over { T }}
UHIGH
- Signal is HIGH for a certain part (t1) of the time interval T and LOW for the remaining time
- Net voltage over T corresponds to the HIGH voltage times the ratio of t1 to T
Image: https://upload.wikimedia.org/wikipedia/commons/thumb/9/9b/Pulse_wide_wave.svg/1280px-Pulse_wide_wave.svg.png

---
Live Demo...
https://commons.wikimedia.org/wiki/File:USAF_EOD_explosion.jpg

---
Serial Data Transfer
- The Arduino Micro has two serial ports:
  - Serial communicats with the computer via USB
  - Serial1 uses the pins RX (receive) and TX (transceive) to communicate with connected devices
- Activity over serial ports is indicated by two LEDs (RX and TX)
- The baudrate has to be defined beforehand and has to match between the devices
  - Arduino: Serial.begin(baudrate);
  - PC: Dropdown menu of Serial Monitor

---
Inter-Integrated Circuit (I²C)
- Bidirectional, serial data bus using the Master/Slave model
- Multiple slaves can be connected to one master
- Requires two lines:
  - Serial Clock (SCL): Controls transfer rate by alternating between HIGH and LOW
  - Serial Data (SDA): Transfers data (one bit per clock cycle)
- The first transferred byte defines receiver an direction

---
Serial Peripheral Interface (SPI)
- Synchronous, serial data bus using the Master/Slave model
- Three common lines:
  - SCLK (Serial Clock)
  - MISO (Master in, Slave out)
  - MOSI (Master out, Slave in)
- One SS (Slave Select) line from the
  Master to each Slave
- Once a Slave is selected by the Master
  (by setting its SS to LOW), it “listens” on MOSI
  and answers over MISO
Image: https://de.wikipedia.org/wiki/Datei:SPI_three_slaves.svg

---
Image: Arduino Forum, User pighixxx, http://forum.arduino.cc/index.php?topic=148734.0