## Slide 1
Sketching with Hardware
06: Programming

## Slide 2
Programming the Arduino
Microcontrollers are restricted in memory and computing power
Programs are written in C or C++
Rather simple applications → simple programs
Different patterns and paradigms than e.g. in Java

## Slide 3
Basic Program Structure
// declare variables here
// the setup routine runs once on startup
void setup() {
}
// the loop routine runs over and over again forever:
void loop() {
}

## Slide 4
Arduino-specific Functions
Function | Description
delay(int micros) | Delays the program by micros microseconds
pinMode(int pin, int direction) | Defines a pin as INPUT or OUTPUT. Should be called during setup().
digitalRead(int pin) | Reads value from a pin. Returns HIGH (1) or LOW (0).
analogRead(int pin) | Reads analog value from a pin. Returns 0 to 255.
digitalWrite(int pin, int value) | Sets a pin to either HIGH (5 V) or LOW (0 V).
analogWrite(int pin, int value) | Sets voltage on a pin to a value between 0 (0 V) and 255 (5 V). Only works with pins that support PWM.
Serial.println(“Hello”) | Writes to the serial monitor and can be used for debugging. Call Serial.begin(9600) during setup().

## Slide 5
Non-blocking code
The Arduino can only run one thread at a time
No parallelization of tasks
The delay()-function blocks the whole program
delay() can be avoided by using a timer

## Slide 6
Simple Timer
int buttonPin = 5;
int ledPin = 13;
int ledState = LOW;
void loop() {
// blink the LED
if(ledState == LOW) {
ledState = HIGH;
}
else {
ledState = LOW;
}
// turn off LED if button is not pressed
if(digitalRead(buttonPin) == LOW) {
ledState = LOW;
}
digitalWrite(ledPin, ledState);
delay(1000); // wait for a second
}
// ...
long lastMillis = 0;
void loop() {
// check time since last update
if(millis() - lastMillis >= 1000) {
lastMillis = millis();
if(ledState == LOW) {
ledState = HIGH;
}
else {
ledState = LOW;
}
}
// turn off LED if button is not pressed
if(digitalRead(buttonPin) == LOW) {
ledState = LOW;
}
digitalWrite(ledPin, ledState);
}
blocking
non-blocking

## Slide 7
Code Structure
Arduino code is often simple and sequential
Tends to get messy pretty fast
Debugging code and hardware at the same time can be tedious
Well-structured code leads to better readability and easier debugging

## Slide 8
State Machine: Cookie Dispenser
#define WAIT 1
#define ORDER 2
#define PAYMENT 3
#define DISPENSE 4
int state = WAIT;
int order;
// cookie dispenser functions
int getInput() { … }
int getOrder() { … }
void handlePayment(int product) { … }
void dispenseProduct(int product) { … }
void loop() {
switch(state) {
case WAIT:
if(getInput() != 0) state = ORDER;
else delay(1000);
break;
case ORDER:
order = getOrder();
state = PAYMENT;
break;
case PAYMENT:
handlePayment(order);
state = DISPENSE;
break;
case DISPENSE:
dispenseProduct(order);
state = WAIT;
break;
}

## Slide 9
Debug Levels
The Arduino IDE has no builtin debugger
Serial output is used to log the state of programs
Using debug levels lets you switch between different levels of verbosity quickly
#define NONE 0
#define ERROR 1
#define WARN 2
#define DEBUG 3
#define ALL 4
#define DEBUG_LEVEL WARN
void loop() {
if(DEBUG_LEVEL >= WARN) {
Serial.println(“Warning!”);
}
}