## Slide 1
Sketching with Hardware
03: Soldering

## Slide 2
Soldering Iron

## Slide 3
Soldering Iron Stand

## Slide 4
Soldering Tip Cleaner

## Slide 5
Solder

## Slide 6
Solder Flux

## Slide 7
Desoldering Pump

## Slide 8
Safety Instructions
The soldering iron gets hot (over 300 °C)
  Do not touch metal parts
  Use the soldering iron stand
  Unplug if not needed anymore
Solder contains lead (which is poisonous)
  Wash you hands after using it (and especially before eating)
Do not inhale the soldering smoke

## Slide 9
Preparation
Make room on your table
Prepare your soldering tools:
  Soldering iron + stand (do not plug it in yet)
  Solder
  Soldering tip cleaner
  Working surface
  Desoldering pump
  Solder flux

## Slide 10
Placeholder: Closeup soldering

## Slide 11
Some tips
Bigger contact area → faster heat transfer
Many components are heat sensitive
  → Try to solder them quickly
Cover wire with solder beforehand (solder flux helps)
Clean the soldering iron before and after use

## Slide 12
Good vs Bad Soldering...

## Slide 13
Live Demo...
https://commons.wikimedia.org/wiki/File:USAF_EOD_explosion.jpg

## Slide 14
Tutorial 02 - Soldering

## Slide 15
Exercise: Mini-Circuit
LED, button, resistor, wire, perfboard
Created with Fritzing

## Slide 16
Approach
Think of a layout beforehand
Bend the component’s legs to fit into the board
Place components on the copperless side of the board
Solder components on the back side
Tip: Begin with resistor and wire as they are more resistant to heat
→ Heat can damage the LED or melt the plastic button

## Slide 17
Testing the circuit
Continuity testing:
  Is everything connected properly?
  Are there any short circuits?
Plugging it in…
  Red wire to 5V (+), Black wire to GND (-)
If it does not work: Troubleshooting
  Correct polarity of the LED?
  Correct resistor?
  Is current flowing?
  ...

## Slide 18
Solution
Created with Fritzing